## Slide 2
SPE-198673-MS AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells
Dmitry Krikunov
Dmitry Lukovkin, Zyfra Oy

## Slide 3
Solution Core
    Modern Electrical Submersible Pumps can be adjusted in a wide variety of oil flow rates. This ability is used by engineers, but they work in a huge level of reservoir feedback uncertainty. They cannot make high-quality predictions about the stability of the operating mode adjusted, fluids composition change, gas ratio and etc.
    Our team has developed a solution that eliminates uncertainties mentioned above and gives recommendations on optimal operating modes automatically.
    Optimization function can be chosen due to the business needs: oil flow rate increase, energy consumption reduction
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov

## Slide 4
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
Outputs and Inputs
We manage
Pump rotation speed
On and off periods
The relationship between work and cost
We predict
Fluid flow rate
Oil flow rate
Gas ratio
Key pump parameters
We track
Pressures
Dynamic Level
Water Cut
Density
Measured oil flow rate
and others
Pump & Well
AI + Traditional
model
We monitor
Pump temperature
Motor current
Load ratio

## Slide 5
Solution background
    Changes to pump operation represent unrealized potential for oil extraction:
    Monitoring of pump operation for oil extraction is performed manually
    Calculation of pump operation is performed manually, which means that, due to limited human perception, maximum oil flow rate cannot be achieved through other modes of operation.
    Changes in pump operation occur rarely, around once per month.
    A reduction in the number of well shutdowns represents unrealized potential for oil extraction:
    The enterprise has no means of reducing the risk of well shutdowns.
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov

## Slide 6
Solution implementation benefits
    Depending on mode needed, the solution gives recommendations for each well to maximize or minimize target function. In both cases benefits are achieved due to the following:
    Predicting liquid and oil flow rate of wells for various ESP modes
    Increase in frequency and automation of telemetry information analysis
    Elimination of human factor in the course of monitoring “problem” wells
    Automated control of recommended ESP modes implementation
    Issuing optimal for oil flow rate modes of ESP operation
    Prioritizing recommendations for savings and rational utilization of staff recourses for well operating modes change used
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov

## Slide 7
Problem statement
To determine ESP mode that provides maximization of well oil rate.
The mode being determined should consist of:
ESP motor frequency
Mode type (Permanent, ARC (autoreclosing), STWO (short-term well operation))
Provisions should be made for penalties and payoffs:
Payoff for high flow rate
Penalty for approaching the parameter limitations (current not more than..., etc.)
Penalty for step change of operating mode
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov

## Slide 8
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
Liquid flow
rate
Water cut
Amount of FPM (formation-pressure maintenance)
water injected into well
Dynamic
level
Artificial Intelligence
Pressures:
Annulus
Intake well head
Buffered
Bottom hole
ESP parameters:
State (on/off)
Current frequency
Voltages
ESP ratings
Inclinometer survey data:
Relative
coordinates
Upper, lower
shooting depth
Elongation, etc.
Data being used

## Slide 9
Conceptual Architecture of the Solution
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
Machine Learning Unit
Data Preparation Unit
ESP Historical Operating Mode Determination Module
Actual Well Flow Rate Module
Data and Rigging Sufficiency Check Module
Well Flow Rate Determination Module
Mode Recommendations Calculation Module
Savings Calculation Module
1
2
3
4
5
6

## Slide 10
Algorithm of flow rate recalculation to actual value is one of the key algorithms of raw data processing.
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
ML
0
24
1
0
24
1
On (1) – off (0) state diagram
On (1) – off (0) state diagram
50Hz
52Hz
50Hz
ESP current frequency diagram
ESP current frequency diagram
Measurement time – 2 h
Measured flow rate – 50 cub. metres/day
Measurement time – 2 h
Measured flow rate – 50 cub. metres/day
Actual flow rate – 47 cub. metres/day
Actual flow rate – 50 cub. metres/day

## Slide 11
ESP Historical Operating Mode Determination Module
Historical data are not marked by types of ESP operating modes. The marking is implemented automatically by corresponding algorithm.
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
0
24
The mode determined by the algorithm: ARC
1
0
24
1
The mode determined by the algorithm: STWO

## Slide 12
Solution Approach
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
ENVIRONMENT MODEL
REAL
ENVIRONMENT
SEARCH AGENT
MODEL GOVERNANCE
model updates
real observations
predicted observations
controls
optimal controls

## Slide 13
Finding optimal control option
Agent searching through possible predicted states for those which lead to maximum value of target function Q:
Rewards for high oil flow rate
Penalizes for constraints approaching
Penalizes for drastic changes in control policy
SPE-198673-MS • AI-based ESP Optimal Control Solution To Optimize Oil Flow Across Multiple Wells • Dmitry Krikunov
con (T)
obs (T-1)
Flow rate (T)
con (T)
max Q (T)
PUMP+ENV MODEL
AGENT

## Slide 14
Thank You / Questions